Pyramid Vector Quantization for Video Coding
Jean-Marc Valin
Daala Coding Party
Sep 2013

---
Motivations
- Pyramid vector quantization is a key technique used in Opus (both SILK and CELT parts)
- Investigate PVQ for a video codec (Daala)
- Potential advantages
  - Preserves energy (details) even when details are imperfect (instead of blurring)
  - Implicit activity masking
  - Better representation of coefficients

---
Gain-Shape Quantization
- Represent a vector as magnitude multiplied by unit-norm vector (radius + point on sphere)
  - Amount of texture vs exact details
- Code magnitude separately
  - Adjust resolution of the sphere based on the magnitude

---
Pyramid Vector Quantizer (PVQ)
- Place K unit pulses in N dimensions
  - Up to N = 1024 dimensions
- Normalize to unit norm (L2)

---
Codebook for N=3 and different K

---
Distortion, N and K
Fewer pulses needed
D = N2/(24K2)

---
PVQ vs Scalar Quantization
-6 dB/bit

---
Prediction
- Unlike CELT, we want to predict the vectors
- PVQ on the residual loses energy preservation
- Apply prediction in the normalized vector
  - Use Householder reflection to align prediction with one axis
  - Encode magnitude of the residual as an angle

---
2-D Projection
Input
Input

---
2-D Projection
Input+prediction
Prediction
Input

---
2-D Projection
- Input+prediction
- Compute reflection plane
Prediction
Input

---
2-D Projection
- Input+prediction
- Compute reflection plane
- Apply reflection
Prediction
Input

---
2-D Projection
- Input+prediction
- Compute reflection plane
- Apply reflection
- Compute/code angle
Prediction
θ
Input

---
2-D Projection
- Input+prediction
- Compute reflection plane
- Apply reflection
- Compute/code angle
- Code other
  dimensions
Prediction
θ
Input

---
Activity Masking
- Artefacts are easier to detect on flat areas they on textured areas
  - Code unit-norm vector with a resolution that depends on the gain (texture)
- Code companded gain gc = g
  - Implicit activity masking built into the bitstream

---
Open Questions
- How to split into bands
- Avoid wasting bits on still video
- Quantization matrix
- Take advantage of correlation/prediction in gain and angle
- Rate-Distortion Optimization
  - Fast RDO PVQ search?